sopale_nested
- version history
- recent feature additions
- multi-nest and its switches

---
sopale
versions
- sopale
  - 1995
- sopale_nested
  - begun 2007
- sopale_nested 2009-07-26_29
  - evolved 2009 -> 2011
- sopale_nested 2011-12-01
  - Fall 2011
- sopale_nested 2012-06-08
  - Summer 2012 (multi nest)

---
version 2011-12-01
features
- boundary condition type 301
- thermal material change

---
version 2012-06-08
motivations
- Initial discussions in August 2011
- After model has run a significant number of time steps, want to:
- 1) create a new nest
- 2) move the nest
- The code internals were hard-coded to 1 nest only, and there was no possibility of adding, removing, or changing, that nest on a restart. So a re-design was required. Not of the calculations, but of the organization of them.

---
while re-designing...1
- Why not more than one nest?
  - [nested]
  - nest_left nest_right nest_top nest_bottom
  - x_ratio y_ratio
  - ...second nest definition
  - ...third nest definition
  - [end] <---- NEW

---
while re-designing...2
- Why not make the array sizes dynamic, so only one build would be required. Separate builds for each grid size (eulerian, lagrangian) are a pain.
  - inject_per_cell 0/? <--- Initial allocation: how many lags per cell
  - inject_increment 4/? <--- when increasing: how many lags per cell
- The requirement that the nest bottom be on the same row as nbzeremesh has been irksome; and is incompatible with the goal of multiple nests. Want to remove that requirement.
- Why not experiment with another matrix solver, e.g. MUMPS. MUMPS is a parallel solver, and might run faster than the current solver (blkfct), which is serial.

---
Spring 2012 additions
- separate velocity calculation for material changes. To avoid spikes in the pressure.
  - matchange_vel_calc yes/no
- Some mechanical loop calculations, that are independant of iteration number, were being repeated in each iteration. Move them to the top of the loop; speed up. This required changes to the boundary condition code, which assumed that said calculations were repeated each iteration.
  - compute_mech_rhs_each_iteration yes/no
  - bc_mech_set yes/no

---
new switches...1
- bc_corners_twice yes/no
- bc_top_nest_mech yes/no
- bc_top_nest_ther yes/no
- compute_plithon_version dec2011/jun2012

---
new switches...2
- lags_to_nest
  - not new, but will have default
- lags_from_nest
  - not new, but will have default
  - code changes underway
- write_combined_eulerian_grid yes/no
- replace_nest before_ALE/after_ALE
  - experimental

---
switches to be removed...1
- eulerian_recolor_calc
- eulerian_recolor_compare
- eulerian_recolor_mod_1
- eulerian_recolor_mod_2
- sediment_recolor_fix

---
switches to be removed...2
- which_interp
- which_lagstoeul
- which_make_weighted_density

---
user guide
- Still formatted for the 6 separate files
- Content upgrade underway. See top 2 switches for an example of the upgrade.